## Slide 1: Improving memory locality in seismic simulations on video cards
Schmidt László Computer engineering BSc
Supervisor : Dr. Reguly István Zoltán

## Slide 2: Motivation
CPU clock reached upper limit.
Trends have shifted towards multithreading
Multi-core CPUs
GPUs can run many parallel threads
Linearly increasing computing capacity

## Slide 3: Parallel
Parallel programming
some instruction can be executed on different CPU core at the same time
Huge initial acceleration, but memory bottlenecks show up quickly.

## Slide 4
The instruction and data must be in the registers
Moving data costs a lot of energy
The farther we want to move it from, the more expensive it is
Reduce the number of expensive operations
Data movement

## Slide 5: Delay of Memory hierarch

## Slide 6: Cross example
1
1
1
1
1
1
1
1
1
1
2
2
3
3
4 x 5 = 20
14 load

## Slide 7: Cross example with blocking
1
1
1
1
1
1
1
1
3
3
3
3
4x5=20 point
12 load

## Slide 8: OpenMP C/C++
Open Multi-Processing
Compile time optimization
Pragmas - message to the compiler
It implements the steps of parallelization
Supports Video Cards
Simple and widespread
https://docs.nersc.gov/development/programming-models/openmp/openmp-resources/

## Slide 9: 3D cross example
Memory locality problem
Lot of points only loaded once
Target teams = GPU
Distribute = among GPU threads
Iterations executed on a gpu

## Slide 10: Loop/Thread/Cache Blocking
Simple implementation on CPU, already widespread
It is not entirely clear in OpenMP
Changing the order of iterations
Team and Thread
Not yet supported in stable compiler versions

## Slide 11: Cross results GPU:Nvidia V100
Naive (default) case 128x1x1 block size
The best case is the block size 8x4x32
Better cache utilization
Less waiting on data
Chart: speedup
| 128x1x1 | 8x4x32 | 4x4x32
Speedup | 1 | 2.1672 | 1.6486
 | Global Hit Rate | Global Load Throughput | Device Memory Read Throughput | L2 Throughput (Reads)
Naive | 36.43% | 1113.80GB/s | 488.21GB/s | 799.30GB/s
Tiled | 71.86% | 1849.00GB/s | 310.39GB/s | 476.74GB/s
improvement | 97% | 66% | 36% | 40%

## Slide 12: Devito
Domain Specific Language (DSL)
Partial differential equations
Python
Compiles to C
OpenMP optimization
Example of sound wave propagation
Seismic Inversion using Devito

## Slide 13: Devito results GPU:Nvidia V100
 | SO 4 | SO 8 | SO 16
128x1x1 | 11.9 | 19.31 | 40.15
16x4x32 | 8.24 | 10.85 | 16.39
Speedup | 1.44 | 1.77 | 2.44
Chart: Soundwave 600^3
| SO 4 | SO 8 | SO 16
128x1x1 | 11.9 | 19.31 | 40.15
16x4x32 | 8.24 | 10.85 | 16.39
Sound wave propagation in 600 ^ 3 space
In a naive case, as the neighbors number grows the time worsens
Tiling improves optimization

## Slide 14: Devito results GPU:AMD MI50
Chart: AMD Acoustic 600^3
| SO 4 | SO 8 | SO 16
Naív | 19.65 | 32.45 | 77.29
Tiled | 17.95 | 27.16 | 70.73
 | SO 4 | SO 8 | SO 16
Naive | 19.65 | 32.45 | 77.29
Tiled | 17.95 | 27.16 | 70.73
Speedup | 1.094 | 1.194 | 1.092
There is no such improvement
Compiler still under development

## Slide 15: Summary
I showed On structured data for neighborhood calculations, how to increase memory locality.
A method for this has been developed in an openMP environment that also works on a GPU.
And I have shown that this can be applied not only to simple examples but also to complex applications (Devito)
  On Nvidia and AMD graphics cards.
  Works with multiple equations.
  This allows devito users to achieve 1.1-2.5x speedup.
As a continuation of my work, I will implement this optimization in the Devito code generation process.